## Slide 1: Parallel Circuits Simulation of Adders
Wenjie Yao
Chengcheng Zhang
Jidong Li
Yiou Zhu

## Slide 2: Overview
Problem Description and Conceptual Model
Implementation of 1-bit Adder
Multi-bit Adders Simulation
Parallel Computation
Experiments and Analysis of Results

## Slide 3: Problem Description
How does a computer add numbers?
Number------Binary Number------Logic Circuit
30+4 00011110+00000100
  AND OR NOT

## Slide 4
Logic Circuit (1-bit adder)
Si = (Ai XOR Bi ) XOR Ci =
Ci+1 = Ai AND Bi OR Ci(Ai XOR Bi) =
Ai | Bi | Sum (Si) | Carry (Ci+1)
0 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 0 | 0
0 | 0 | 0 | 0
30: 00011110
4: 00000100
34: 00100010

## Slide 5
Entities:
Resource:
Whole Simulator: combination of multiple 1 bit adder
Each 1-bit adder: consisting of several AND/OR/NOR/XOR gates.
Consumer:
Digits of the specific pairs of numbers Ai, Bi. And the output from the last adder Ci.
Queue: queue of numbers waiting for processing.
queues of digits waiting to enter each 1-bit adder.
Attributes:
Data: numbers and their digits.
Timestamp of each number.
Precision of the input numbers in binary form.
Conceptual model

## Slide 6
Events:
Receive a message from the last 1-bit adder.
Process digits Ai, Bi, Ci using AND/OR/NOR/XOR gates
Send a message to the next 1-bit adder
Activity: Executing a pair of digits, beginning with receiving the message from the last 1-bit adder and ends with getting the summary and sending a message to the next 1-bit adder.
Conceptual model

## Slide 7: How to realize a 1-bit adder in C++

## Slide 8
Gnode: logic gates (NOT, OR, AND)
SimObj: data and basic function for GNode
Event: electric signal
Graph: one-bit adder, 15 GNodes
Classes

## Slide 9
Code Structure
SimObj
GNode
InNeighbour/outNeibour
Input
InputEvents
InputTimes
clock
RecvTime
Value(0,1)
Event

## Slide 12
Time control
0
0
1
1
1
5(1)

## Slide 13
When adding a pair of numbers, each Full Adder (1-bit adder) can operate independent but sequentially.
Architecture of Multi-bit Adder
Queue

## Slide 14
Assume that:
A_ij, B_ij=the jth digit of the ith number
C_ij=the overflowed number from the jth digit of the ith number
Parallel Computing

## Slide 15
What can we do with the results?

## Slide 16
Take an example with 31+37=68
(in binary expressions 00011111+00100101=01000100)
Graph[6] Node[13] output=1 time=18
Validation and Verification

## Slide 17
Graph | Node[13] | Node[14]
0 | 0 | 1
1 | 0 | 1
2 | 1 | 1
3 | 0 | 1
4 | 0 | 1
5 | 0 | 1
6 | 1 | 0
7 | 0 | 0
Outputs in Time=18

## Slide 18
Graph | Input a | Input b | Input c | “And” gate output=1
0 | 1 | 1 | 0 | 11
1 | 1 | 0 | 1 | 10
2 | 1 | 1 | 1 | 12
3 | 1 | 0 | 1 | 10
4 | 1 | 0 | 1 | 10
5 | 0 | 1 | 1 | 8
6 | 0 | 0 | 1 | 6
7 | 0 | 0 | 0 | \
Focus on the “and” gates of each graph

## Slide 19
Results change over time

## Slide 20
Bits | Convergence time |  |  |  |  |  |  |  |  | 
2 | 2 | 4 | 1 | 3 | 2 | 1 | 4 | 3 | 1 | 1
3 | 5 | 2 | 5 | 4 | 4 | 3 | 1 | 3 | 3 | 5
4 | 5 | 4 | 5 | 2 | 11 | 2 | 3 | 5 | 7 | 5
5 | 5 | 2 | 3 | 4 | 6 | 8 | 3 | 3 | 9 | 5
6 | 8 | 5 | 11 | 10 | 7 | 3 | 3 | 3 | 8 | 12
7 | 16 | 9 | 19 | 20 | 8 | 8 | 9 | 5 | 5 | 10
8 | 10 | 9 | 8 | 9 | 5 | 8 | 8 | 11 | 10 | 13
Relationship between convergence time and bits

## Slide 21
ANOVA based on Bayesian way (normal prior)

## Slide 22: Q & A

## Slide 23: Thank you!